## Slide 1: Pulse Code Modulation
Fathima, Noor Afshan
A20385838

## Slide 2: Pulse Code Modulation
DEFINITION: Pulse code modulation (PCM) is essentially analog-to-digital conversion of a special type where the information contained in the instantaneous samples of an analog signal is represented by digital words in a serial bit stream.
The advantages of PCM are:
  Relatively inexpensive digital circuitry may be used extensively.
  PCM signals derived from all types of analog sources may be merged with data signals and transmitted over a common high-speed digital communication system.
  In long-distance digital telephone systems requiring repeaters, a clean PCM waveform can be regenerated at the output of each repeater, where the input consists of a noisy PCM waveform.
  The noise performance of a digital system can be superior to that of an analog system.
  The probability of error for the system output can be reduced even further by the use of appropriate coding techniques.

## Slide 3: Sampling, Quantizing, and Encoding
The PCM signal is generated by carrying out three basic operations:
      Sampling
      Quantizing
      Encoding
Sampling operation generates a discrete signal.
Quantizing operation approximates the analog values by using a finite number of levels. There are two types: Uniform and Non-Uniform
PCM signal is obtained from the quantized stepped signal by encoding each quantized sample value into a digital word.

## Slide 4: Analog to Digital Conversion
The Analog-to-digital Converter (ADC) performs three functions:
  Sampling
    Makes the signal discrete in time.
  Quantization
    Makes the signal discrete in amplitude.
    Round off to one of q discrete levels.
  Encode
    Maps the quantized values to digital words that are  bits long.
Sample
Quantize
Encode
Analog
Input
Signal
ADC
111
110
101
100
011
010
001
000
Digital Output
Signal
111 111 001 010 011 111 011

## Slide 5: Quantization Example
Analogue signal
Sampling TIMING
Quantization levels.
Quantized to 5-levels
Quantization levels
Quantized 10-levels